## Slide 1: Knock Detection Reference Code Specification
Steve.Han
17.06.2015

## Slide 2: SW concept
DMA
Anti aliasing FIR
Knock detection FIR(Coefficient is decide by HMC ASW)
DMA
Conventional
New developed

## Slide 3: SW Operation
CRANK
KNOCK_WINDOW
DATA_IN
AFTER_DSP

## Slide 4: SW Design detail concept-Data generation
DSADC is triggered, when Knock window is high.
Interrupt is generated, when each data is created.

## Slide 5: SW Detail design concept-Trigger connection
DSADC
DMA
DSADC IR is connected to DMA Hardware request.

## Slide 6: SW Detail design concept-Double buffering
Using DMA, Generated DATA at DSADC is moved to destination.
At here , DMA use Double buffering functionality.
DMA destination is automatically switched from one to the other when data is filled fully.
CRANK
KNOCK_WINDOW
DATA_IN
These are buffer switch point.

## Slide 7: SW Detail design concept-Data transfer
RROAT = 0;
TSRz.CH is reset after each transfer. A transfer request is required for each transfer
CHMODE = 1;
Continuous Mode operation is selected for DMA channel z.
After a transaction, bit TSRz.HTRE remains set

## Slide 8: SW Detail design concept-Signal processing
DSP lib Ifx_firRealQ15a is called, when buffer is full
It takes 115.326us(128 Data)
CRANK
KNOCK_WINDOW
DATA_IN
AFTER_DSP

## Slide 9: SW Detail design concept-Ignore data
Considering Group Delay, 10 data is ignored.

## Slide 10: SW Detail design concept-ISR
Knocheck_Window_ISR is called, when window open or close
DMA_FULL_ISR is called, when buffer is full

## Slide 11: Dynamic view

## Slide 12: ISR Flowchart

## Slide 13: Module Interface

## Slide 14: Folder structure
knocheck_config.h: All system dependent defines are in here.
knocheck_def.h: General knock dependent defines, structures, enums are in here.
knocheck_dma_def.h: DMA dependent defines, structures, enums are in here.
knocheck_dsadc_def.h: DSADCdependent defines, structures, enums are in here.
knocheck_priv.h: Knock module extern, includes are in here.
knocheck_pub.h: Interface function and values are in here. Other modules are can access this module only through this header file.
knocheck_dma.c: DMA Initialization functionality is in here
knocheck_dsadc.c: DSADC Initialization functionality is in here
knocheck_glovar.c: All global values are in here
knocheck_sigpro_isr.c: IR is occurred, when destination buffer is full. Accumulate datas are filter calculated at here.
knocheck_win_isr.c: IR is occurred, when window open or close. Accumulate datas are filter calculated at here.
knocheck_win.c: Knock Window Initialization functionality is in here

## Slide 15: Test Result-Window length change

## Slide 16: Test Result-Module Enable

## Slide 17: Test Result-DSADC measurement
Calculated Value
Measurement Value

## Slide 18: Test Result-Data input validation
1111:buffer 0
2222:buffer 1
3333:Window close buffer 0
4444:Window close buffer 1
Input data order

## Slide 19: Test Result-Signal processing