## Slide 1: Knock Detection Reference Code Specification
Steve.Han
28.07.2015

## Slide 2: SW concept
DMA
Anti aliasing FIR
Knock detection FIR(Coefficient is decide by HMC ASW)
DMA
Conventional
New developed

## Slide 3: SW Operation
CRANK
KNOCK_WINDOW
DATA_IN
AFTER_DSP

## Slide 4: SW Design detail concept-Data generation
DSADC is triggered, when Knock window is high.
Interrupt is generated, when each data is created.

## Slide 5: SW Detail design concept-Trigger connection
DSADC
DMA
DSADC IR is connected to DMA Hardware request.

## Slide 6: SW Detail design concept-Double buffering
Using DMA, Generated DATA at DSADC is moved to destination.
At here , DMA use Double buffering functionality.
DMA destination is automatically switched from one to the other when data is filled fully.
CRANK
KNOCK_WINDOW
DATA_IN
These are buffer switch point.

## Slide 7: SW Detail design concept-Double buffering
Using DMA, Generated DATA at DSADC is moved to destination.
At here , DMA use Double buffering functionality.
DMA destination is automatically switched from one to the other when data is filled fully.
CRANK
KNOCK_WINDOW
DATA_IN
If user want to check BUFFER NUM in ISR to know what is filled with data, Return value is current working BUFFER NUM. So user should use
Opposite NUM BUFFER.
But if DMA is not working, User can use Buffer num directly.

## Slide 8: SW Detail design concept-Data transfer
RROAT = 0;
TSRz.CH is reset after each transfer. A transfer request is required for each transfer
CHMODE = 1;
Continuous Mode operation is selected for DMA channel z.
After a transaction, bit TSRz.HTRE remains set

## Slide 9: SW Detail design concept-Signal processing
DSP lib Ifx_firRealQ15a is called, when buffer is full
It takes 115.326us(128 Data)
CRANK
KNOCK_WINDOW
DATA_IN
AFTER_DSP

## Slide 10: SW Detail design concept-Ignore data
Considering Group Delay, 10 data is ignored.

## Slide 11: SW Detail design concept-ISR
Knocheck_Window_ISR is called, when window open or close
DMA_FULL_ISR is called, when buffer is full

## Slide 12: Dynamic view

## Slide 13: ISR Flowchart

## Slide 14: Module Interface

## Slide 15: Folder structure
knocheck_config.h: All system dependent defines are in here.
knocheck_def.h: General knock dependent defines, structures, enums are in here.
knocheck_dma_def.h: DMA dependent defines, structures, enums are in here.
knocheck_dsadc_def.h: DSADCdependent defines, structures, enums are in here.
knocheck_priv.h: Knock module extern, includes are in here.
knocheck_pub.h: Interface function and values are in here. Other modules are can access this module only through this header file.
knocheck_dma.c: DMA Initialization functionality is in here
knocheck_dsadc.c: DSADC Initialization functionality is in here
knocheck_glovar.c: All global values are in here
knocheck_sigpro_isr.c: IR is occurred, when destination buffer is full. Accumulate datas are filter calculated at here.
knocheck_win_isr.c: IR is occurred, when window open or close. Accumulate datas are filter calculated at here.
knocheck_win.c: Knock Window Initialization functionality is in here

## Slide 16: Test Result-Window length change

## Slide 17: Test Result-Module Enable

## Slide 18: Test Result-DSADC measurement
Calculated Value
Measurement Value

## Slide 19: Test Result-Data input validation
1111:buffer 0
2222:buffer 1
3333:Window close buffer 0
4444:Window close buffer 1
Input data order

## Slide 20: Test Result-Signal processing

## Slide 21: Test Result-Not integrate data
Receive the 128 data, but these data not participate to integration calculation.

## Slide 22: Test Result-Not integrate data
Data input check test pass

## Slide 23: Test Result-Execution time test
1ms OS Task 수행주기
128Data 입력에 대한 FIR 처리
31~40 Data 입력에 대한 FIR 처리

## Slide 24: Test Result-Gain test
INCFGP, INCFGN, GAINSEL, INSEL, INMODE, INMAC 접근관리 비트인 INCWC가 미반영 되어 버그 발생.
아래와 같이 SW 업데이트

## Slide 25: Test Result-Frequency test
.60~100Khz sweep for 30s
.0~140Khz sweep for 50s
.40~140Khz sweep for 30s
DMA data
After Filterdata

## Slide 26: Test Result-Frequency test
.10~200Khz sweep for 30s

## Slide 27: Test Result-Frequency test
.104Khz 에서 Integration 값이 급격하게 변화면서 1KHz 단위로 값이 급격하게 변하기 시작

## Slide 28
.10~200Khz sweep for 30s